## Slide 1
Real-Time Multi-Person Opt-in Camera System
Complete Flow Diagram and Implementation Details

## Slide 2
Method Summary: Bridging Asynchronous Data
Data Fusion Challenge
Integrating sparse 3 FPS UWB localization with high-rate 30 FPS camera tracklets in real-time.
UKF as Temporal Bridge
Dedicated Unscented Kalman Filter for each UWB tag upsamples to 30 FPS with uncertainty weighting.
Probabilistic Matching
Mahalanobis distance calculates similarity between UKF position and camera observation over sliding window.
Optimal Assignment
Linear Assignment Problem solver finds best one-to-one match between all UWB tags and camera tracklets.
The system achieves robust, real-time person identification by decoupling high-rate tracking (UKF at 30 FPS) from lower-rate identification (LAP at 10 FPS), optimizing both latency and stability.

## Slide 3
Complete System Flow Diagram
Data Sources
Camera Tracklets (30 FPS)
UWB Measurements (3 FPS)
Multi-Person Tracker (30 FPS)
MultiPersonTracker
UKF Prediction (All Tags)
UKF Update (UWB-Driven)
UKF State Buffer (30 FPS)
Camera Tracklet Buffer
Trajectory Matching (10 FPS)
Calculate Mahalanobis Cost Matrix
Solve LAP (Hungarian Algorithm)
Optimal Assignment (UWB ID -> Tracklet ID)
Final Identified Persons (10 FPS)
UKF States (Pos + Cov)
Tracklet Data
Assignment (10 FPS)
Visual representation of the real-time inference pipeline executed every frame (30 FPS). Data flows from asynchronous sources through multi-person tracking to final identification (10 FPS).

## Slide 4
Implementation: Multi-Person Tracker
Class Overview
Class Name
MultiPersonTracker
Core Structure
Dictionary of StreamingUWBUKF2D instances, keyed by UWB ID (101, 102, ...)
State Vector (4D)
s = (x, v_x, y, v_y) Position + Velocity
UWB Update Trigger
Only when new UWB measurement arrives (3 FPS). Uses UWB position as observation.
Operational Flow
predict_all(frame, timestamp)
Runs for all active UKF instances
Executes every frame (30 FPS)
→
→
→
update_all_uwb(uwb_measurements)
Updates only when UWB data available
Corrects predicted state with measurement
→
→
→
Occlusion Handling
When person leaves frame, UKF continues predicting. Covariance grows, reflecting increased uncertainty. Identity maintained until re-entry.
Each UWB tag maintains its own UKF instance, enabling independent, parallel tracking of multiple persons with automatic identity preservation during occlusions.

## Slide 5
Implementation: Real-Time Matching
Matching Rate
Runs at 10 FPS (every 3 frames) to reduce computational load and increase temporal stability.
Sliding Window
Similarity calculated over 1-second window (30 frames) of recent data, not entire trajectory.
Cost Function
Mahalanobis Distance D(p_i, p_j) weighted by UKF covariance matrix.
LAP Feasibility
Infinite costs replaced with MAX_COST (1000.0) to ensure solver convergence.
Mahalanobis Distance
D = √[(p_uwb - p_cam)ᵀ × Σ⁻¹ × (p_uwb - p_cam)] where: • p_uwb = UKF position • p_cam = Camera position • Σ = UKF covariance
Similarity Score
Similarity = 1/(1 + D) Range: [0, 1] • 1.0 = Perfect match • 0.0 = No match
The RealTimeTrajectoryMatcher solves the Linear Assignment Problem (LAP) using the Hungarian algorithm to find the optimal one-to-one match between all active UWB tags and all visible camera tracklets, maximizing total similarity while maintaining real-time performance.

## Slide 6
Key Features and Robustness
✓ Multiple Targets
Simultaneously tracks and identifies multiple UWB-tagged persons with independent trajectories and assignments.
→ Late Arrivals
Dynamically initializes tracking for persons entering the scene after the system starts, with automatic UKF convergence.
◆ Independent Occlusions
Handles each person's occlusion independently. UKF continues predicting while maintaining identity during temporary frame absence.
✗ Distractor Rejection
Correctly rejects camera tracklets without UWB tags, preventing false assignments to non-opted-in persons.
Real-Time Performance Metrics
0.95 ms
Avg Frame Time
33.33 ms
30 FPS Budget
✓ MET
Real-Time Status

## Slide 7
Conclusion: Innovation and Impact
Decoupled Architecture
High-rate UKF tracking (30 FPS) decoupled from lower-rate LAP identification (10 FPS) optimizes both latency and stability.
Robust Multi-Target
Successfully handles multiple simultaneous targets, late arrivals, independent occlusions, and distractor tracklets.
Real-Time Performance
Average processing time of 0.95 ms per frame, well below the 33.33 ms constraint for 30 FPS operation.
Privacy-Preserving
Records only individuals who explicitly consent via UWB tag opt-in, ensuring privacy compliance and ethical deployment.
The decoupled architecture provides a robust, scalable solution for privacy-preserving person identification in dynamic, real-world scenarios. Ready for deployment on vehicle-mounted platforms and edge devices.